## Slide 1: Using Mantid with muon experiments, instruments and data
James Lord and Anthony Lim

## Slide 2: Muon interfaces

## Slide 3: Frequency Domain
Muons precess in a magnetic field
  Oscillation in spectra
Internal fields in magnets and superconductors
Hyperfine coupling of muonium in semiconductors
  Example here: TiO2 crystal, with TF 200G

## Slide 4: FFT
Group data, or use PhaseQuad
Transform.
TF data:
  Complex inputs
  Peaks give sign of local fields
LF data:
  Only F-B asymmetry
  Unsigned |B|

## Slide 5: Maximum Entropy
Best Fit of a spectrum to reconstruct the data
Muon version
  One spectrum for the whole run
  Detectors have their own phases and amplitudes
Optimise the resolution and signal-to-noise

## Slide 6: 2D plot
ConjoinSpectra to get 2D plot of intensity vs. field and temperature
Splitting of sidebands clearly visible

## Slide 7: Magnetism
Ideal case: one frequency
Easy to fit in time domain
Real life: complex structure
Frequency domain helps

## Slide 8: Simulation supporting Analysis …
Knowledge of the muon site often key to detailed interpretation
Calculation package (MuESR) developed to predict muon sites
Python library running under Mantid
Being developed as part of the EU funded SINE2020 project
Measurements
Calculations
+
Site prediction / Interpretation

Example from A. Amato et al, PRB 89, 184425 (2014)
MnSi;
‘red’ – µ+

## Slide 9: Simulations
QUANTUM program to model muon spins interacting with sample
Originally stand alone FORTRAN .exe
  Inputs from dialog boxes
  Output to files, plot in another package
Rewritten in Python using NumPy
Mantid algorithm
  Input table to define model (flexible)
  Save / load / edit tables or create from script
  Output to Workspaces
In the Script Repository

## Slide 10: Simulation and Fitting
QUANTUM simulation also works as a fit function
Use within Muon Analysis, Muon ALC or a script
Vary model parameters to optimise fit
Simultaneous model/fit at several magnetic fields or temperatures
  Model parameters tied together
  Field inputs set from log values

## Slide 11: QUANTUM example
Model definition table
Data and fit

## Slide 12: Simultaneous fits
10mM Benzene in hexane
335K, 10G field steps
352 total parameters
110 fixed, 227 tied, 15 free

## Slide 13: Simulations for experiment planning
Silicon, with two muon sites
Electron picked from conduction band forming muonium
Try polarising electrons with laser
What effect might we expect on the muon signal?
Which magnetic field should we use?
Run simulations in cabin with users waiting to start taking data

## Slide 14: Instrument View for diagnostics
Direct plot with time slicing
Positrons from separator leaking through shielding
Muons stopping in beam pipe and collimator

## Slide 15: View of processed data
Script to process data
Output Workspace still has instrument definition
Phase of TF signal per detector

## Slide 16: The script repository
Algorithms
Fitting functions
External packages (e.g. MuESR)

## Slide 17: Advantages of the script repository
User generated scripts
Instant access for users
Can be auto-loaded into Mantid
Can reduce development time

## Slide 18: Development process
Understand requirements and theory
Write code to do calculation
Verify code is correct
Write unit tests and documentation
Code review and developer testing
Review improvements
Made available in the nightly

## Slide 19: Development process
Understand requirements and theory
Write code to do calculation
Verify code is correct
Write unit tests and documentation
Code review and developer testing
Review improvements
Made available in the nightly
Tried out by scientists
Additional requirements or changes requested

## Slide 20: Development process
Understand requirements and theory
Write code to do calculation
Verify code is correct, with scientists
Write unit tests and documentation
Code review and developer testing
Review improvements
Made available in the nightly

## Slide 21: MuonMaxent
Code written by James Lord
Based on Fortran version widely used in the muon community
Significantly reduced time to get into code base
Now integral to the new muon Frequency Domain GUI

## Slide 22: Development process
Understand requirements and theory
Write code to do calculation
Verify code is correct
Write unit tests and documentation
Code review and developer testing
Review improvements
Made available in the nightly

## Slide 23: Development process
Understand requirements and theory
Write code to do calculation
Verify code is correct
Write unit tests and documentation
Code review and developer testing
Review improvements
Made available in the nightly
✔
✔
✔
Clean up code

## Slide 24: Getting involved
Ask for code to be added to Mantid
Will cite your paper/DOI and/or give credit in the documentation